## Slide 2: DAA-Optimized Optical Node Forward-Looking & Futureproof

## Slide 3: DAA-Optimized Node
Forward-looking, futureproof solution that enables MSOs to begin to capitalize on the capabilities of Distributed Access Architecture (DAA) and digital technologies, while seamlessly accommodating future technologies and architectures as they become available

## Slide 4: New Housing Features
Purpose Built to Support DAA and Future Technologies
Supports 2 GHz “Extended Spectrum DOCSIS”
Supports for Full Duplex DOCSIS
Designed to dissipate >180 Watts
Diagonal External Fin Design - optimized heat dissipation in any mounting orientation
Four RF/AC ports and two AC/Local insertion ports
Forward/Return test points on each RF port
Multi-function adapter port for future applications
  (e.g. WiFi, 5G)
LH Side
RH Side
Fiber Entry
Ports
Multi-function
Adapter Port
FWD/RTN
Test Point
AC / RF Local Insertion
AC / RF Ports

## Slide 5: Node Configuration
Four Independent RF Modules
  Only populate active ports for cost savings
  High output level - 58 / 37 dBmV 1218 / 105 MHz referenced to QAM (64 / 43 “virtual”) with DPD power reduction
  Plug-in diplex filters (standard split frequencies)
All Electronic Attenuators & Equalizers
  Eliminate plug-ins
  Support auto-alignment & remote control
Dual Redundant High-Efficiency Power Supplies
Supports Up To Two RPD/RMD Modules with Analog RF Overlay Option

## Slide 6: RPD/RMD Module - Interfaces
Four Discrete Forward and Return Path RF Interfaces
  Eliminates RF configuration/combining modules
  Segmentation configured in digital domain
Four Discrete Performance Monitor Ports
  Per port Digital Predistortion (DPD) to optimize each individual forward path hybrid
  DOCSIS PNM Full-band Capture 5 to 1218 MHz
  On-board spectrum analysis supports auto-alignment
Up to Four SFP+ Interfaces Supporting Daisy Chain
Forward and Return Path Test Points
LED Diagnostics
  System & Power status, SFP activity, RF Port enabled

## Slide 7: RPD / RMD Module – Segmentation Capacity
Downstream 1 or 2 service groups with combination of the following per service group:
  Six 192 MHz OFDM channels
  160 SC QAM channels
  10 OOB channels & 16 tone generators
Upstream 1, 2 or 4 service groups with combination of the following per service group:
  Up to 199 MHz per service group
  Two 96 MHz OFDMA channels
  24 ATDMA or 16 ATDMA + 8 SCDMA channels
  6 OOB channels

## Slide 8: Node Management
CM-SP-R-OSSI compliant for RPD module configuration
Secure Auxiliary Core application to support traditional node MIB functions
  SCTE HMS monitoring MIBs
  DOCSIS PNM MIBs
  RF configuration and auto-alignment
  Barcode inventory scan
  Disable unused RPD/RMD module functions for power savings